Equipment Innovations

OWNER’S MANUAL

PC-14

50A Plasma Cutter

Adjustable From 0-50A

Please read carefully before your operation

-1-

TABLE OF CONTENTS

INTRODUCTION

WARNING AND SAFTY PRECAUTIONS

Plasma

Plasma Defined

Voltage Regulation

Thermal Protection

Duty Cycle

Input Power

MAIN TECHNIAL DATA

INSTALLATION

Unpacking

Operating Environment

Input Cable Connection

TORCH AEEEMBLY

Torch Assembly Procedure

OPERATION

To Begin

Cutting

Stand-off Cutting

Piercing

MAINTENANCE

Each Use

Weekly

TROUBLE SHOOTING

FRONT/BACK VIEW AND CONSUMABLES-2-

INSTALLATION

- Input Power

  - This machine has automatic voltage detection for 110/220V

- Input Wiring

  - Improper wiring may cause internal damage to the machine and will void any warranty.

    - For 110V

      - Black or brown= Live

      - White or green = Neutral or

      - Yellow/Green = Earth or Ground

    - 220V

      - Black or brown = Live

      - White or green = Live or green wire

      - Yellow/Green = Earth or Ground

- Torch Assembly

  - This machine uses compressed air as the cutting gas.

  - DO NOT use anything other than compressed air

  - Acceptable air pressure is 50-80psi

  - Recommended most effective is 60psi

# AIR REGULATOR SETUP

- Connect the hose to the back of the machine

- Install the regulator to the back of the machine using small screws

- Connect the hose to the regulator

- Install the pressure gauge

TORCH ATTACHMENT

Torch attachment should only be installed with the machine turned OFF.

- Slide the insulation piece over the torch cable.

- Connect the torch cable to the machine.

- Connect the insulation piece to the machine.

MAINTENANCE

- Each Use

  - With the power turned off.  Before and after each use inspect the machine and its torch.

  - Replace or repair any worn part prior to use.

  - A worn out tip is characterized by an oversized or elongated orifice.

  - If the electrode is recessed greater than 1/8” it should be replaced.

  - If the shield cup is not able to be put on easily it may need to be replaced.

- On a weekly basis the machine should be blown out for dust

TROUBLESHOOTING

| Problem | Cause | Solution |
| --- | --- | --- |
| Torch doesn’t turn on | Power switch is off Problem with air supply Ground clamp not attached | Turn power switch ON Check air supply Properly attach ground clamp |
| Sparks Shooting Upward | Plasma torch not piercing material Torch is too far from material Improper grounding of material Speed | Increase the current. Decrease the distance between the torch and cutting stock Properly attach the ground clamp or move ground clamp closer to work Slow down and reduce cutting speed |
| Dross build up | Material/tool is too hot Current is too high Cutting speed is too slow Worn out torch parts | Allow time for material/tool to cool down Reduce current Increase cutting speed Turn machine off. Inspect and replace consumables as necessary. |
| Arc stops during cut | Cutting speed is too slow Torch is too far from material Worn out torch parts Improper grounding of material | Increase cutting speed Decrease the distance between the torch and the stock Turn machine off. Inspect and replace consumables as necessary. Properly attach the ground clamp or move ground clamp closer to work |
| Low penetration | Cutting speed is too fast Torch is tilted too far Metal too thick Worn out torch parts | Reduce cutting speed Adjust torch position More than one pass may be needed Input current of machine may be insufficient Turn off machine. Inspect and replace consumables as necessary. |
| Consumables wear out too quickly | Unit capability is exceeded Pilot Arc time is excessive Improper air supply | If the material is too thick you should increase the torch angle to prevent blowback into the tip of the torch The maximum recommended time for pilot is 5 seconds. Check air supply, operating pressure should be ~60psi Check your air compressor |